## Slide 1: GOES-R Hurricane Intensity Estimation (HIE) Validation Tool Development
Winds Application Team Tim Olander (CIMSS)
Jaime Daniels (STAR)
Notes: This presentation should reflect your current plans (and schedule) for the development of product validation tools (routine & deep-dive) for each of your products

## Slide 2: OUTLINE
Products (1-2 slides)
Validation Strategies (3-4 slides)
Routine Validation Tools (4-5 slides)
“Deep-Dive” Validation Tools (4-5 slides)
Ideas for the Further Enhancement and Utility of Validation Tools (1-2 slides)
Summary
Notes: Plan on a 15-20 min presentation. Slide counts per topic area are provided as guidance. Slide counts will vary depending upon number of products and tools.

## Slide 3: Products
The Hurricane Intensity Estimation (HIE) algorithm produces tropical cyclone (TC) intensity estimates using long-wave infrared imagery (GOES-R Channel 13 : 10.1-10.6µm).
Algorithm specifications
  Full disk coverage at 2km horizontal resolution for all active TC every 30 min.
  Accuracy/Precision requirements : 6.5/8.0 m/s
Project stakeholders include
  NOAA/NWS/National Hurricane Center (NHC) and Central Pacific Hurricane Center (CPHC)
  NOAA/NESDIS/Satellite Analysis Branch (SAB)
  Department of Defense/Fleet Numerical Meteorology and Oceanography Center (FNMOC) and Joint Typhoon Warning Center (JTWC)
  Various International (WMO) Tropical Forecast Centers including BoM (Australia), Fiji, JMA, India, and MeteoFrance
Notes:   Provide a list of products and their specifications (spatial and temporal resolution, coverage). Include an example display(s) of your products.
  JD Comments:
  Change ”global” coverage” to “FD” coverage. FD is the only geographic coverage rqmt I believe..

## Slide 4: Products
HIE algorithm output is purely textual (specifically it consists of the current TC intensity in terms of wind speed in m/s). No product displays are required. Examples of output “Tailored Products” are provided.
History File Listing
Current Intensity “Bulletin”
Notes:   Provide a list of products and their specifications (spatial and temporal resolution, coverage). Include an example display(s) of your products.

## Slide 5: Validation Strategies
Initial HIE Validation suite was delivered 15 December 2010.
  No feedback or comments have been provided by reviewers as of yet.
HIE intensity estimates (stored in HIE history files) can be validated against two different “ground truth” data sets either in real-time of post-storm, depending on the data set used in the process.
  In situ aircraft reconnaissance measurements of maximum wind speed.
    May not be available for part or all of the storm lifetime, depending on where the storm track is located.
  “Working” and “Final” Best Track storm intensity history.
    Available for entire storm lifetime, but may not be based entirely on in situ data.
    Working Best Track is available in real-time during the storm lifetime. It may not be accurate due to bad observational data, inaccurate Dvorak estimates, or TC forecaster error.
    Final Best Track are made available after extensive analysis of all in situ observations, estimates from remote sensing methods/applications, and TC forecast methodology have been examined.
  “Ground Truth” data can be easily obtained via NOAA “Family of Services” or FTP sites (such as NOAA/NHC)
Notes:   Highlight/summarize validation strategy for each product.
  Identify reference/”ground truth” datasets that are needed and where/how these are obtained
  Identify validation tools (routine & deep-dive) that are needed and being developed

## Slide 6: Routine Validation Tools
Datasets will include the HIE history file output for each storm being analyzed. The history files will be compared directly to the in situ aircraft reconnaissance measurements of TC intensity or the Best Track intensity for the storm in question.
The HIE validation suite will produce statistical comparisons of the HIE intensity estimates and the validation data. The statistical analysis will be provided in terms of wind speed (in m/s) precision and accuracy metrics as well as additional error metrics utilized at operational NOAA TC forecasting and analysis centers.
HIE Validation analysis suite submitted/proposed has already been used by an operational TC forecast center (NOAA/SAB) to verify the ADT/HIE, so it is already familiar to organizations who wish to validate the HIE.
Output products are ASCII text files derived using a series of C programs and shell scripts. No proprietary software is currently used.
Notes:   For each product, describe and illustrate the routine validation tools that you have or are developing. At a minimum address the following:
  - Capabilities (in their final state)
  - Datasets used
  - Visualization software tools used (IDL, McIDAS, other…) to visualize the products, intermediate products, diagnostic data, product performance measures, reference/”ground-truth” data, etc…
  -

## Slide 7: Routine Validation Tools
Current intensity validation statistical output example
  Intensity statistical error analysis versus ‘ground truth” (either reconnaissance and/or NHC Best Track information)
  Accuracy and precision measurements are displayed for the storm in question
  Categorical differences in ADT differences from “ground truth” can provide quick overview of any intensity estimate biases
  Output layout mirrors output parameters as utilized in operations by NOAA/SAB
INTENSITY ERRORS (wind speed : m/s)
bias rmse aae stdv cnt
ADT:07L 2.04 7.33 5.61 7.04 23
ADT-BestTrack Intensity Differences
dCAT ALL TD TS H12 H35
<-20 0 0 0 0 0
-20 0 0 0 0 0
-15 1 0 0 0 1
-10 1 0 0 0 1
-5 4 0 1 1 2
0 9 0 1 6 2
+5 4 0 0 1 3
+10 2 0 0 0 2
+15 2 0 0 0 2
+20 0 0 0 0 0
>+20 0 0 0 0 0
23 0 2 8 13
dCAT ALL TD TS H12 H35
<= 2.5: 39.1% 0.0% 50.0% 75.0% 15.4%
<= 7.5: 73.9% 0.0% 100.0% 100.0% 53.8%
>10.0: 17.4% 0.0% 0.0% 0.0% 30.8%
Notes:   For each product, describe and illustrate the routine validation tools that you have or are developing. At a minimum address the following:
  - Capabilities (in their final state)
  - Datasets used
  - Visualization software tools used (IDL, McIDAS, other…) to visualize the products, intermediate products, diagnostic data, product performance measures, reference/”ground-truth” data, etc…
  -

## Slide 8: ”Deep-Dive” Validation Tools
Further statistical analysis comparisons will be derived versus various operational tropical cyclone forecast center intensity estimates
  Manual/Subjective Dvorak Technique estimates will also be compared to automated HIE estimates to note/define biases and/or derive baseline accuracy threshold for Dvorak-based methodologies
    NOAA/Satellite Analysis Branch (SAB) and NOAA/NHC/Tropical Analysis and Forecast Branch (TAFB), as well as the Joint Typhoon Warning Center (JTWC) currently perform manual Dvorak TC intensity estimates
  Methods to obtain real-time “ground truth” measurements of intensity and current operational Dvorak estimates would need to be outlined
  Output will be created using any graphical software package since data is based upon simple ASCII data files
Analysis of HIE automated storm center determination algorithm will also be provided
  Proper determination of storm center plays large role in intensity accuracy
  Graphical displays can easily show impact of improved position over forecast
  Statistical analysis can provide accuracy of each different location method
Notes:   For each product, describe and illustrate the “deep-dive” validation tools that you have or are developing. At a minimum address the following:
  - Capabilities (in their final state)
  - Intended use
  - Datasets used
  - Visualization software tools used (IDL, McIDAS, other…) to visualize the products, intermediate products, diagnostic data, product performance measures, reference/”ground-truth” data, etc…
  Comments (JD)
  :
  1) This slide should be able to say specifically what “deep-dive” tools are being developed (ie., as in the HIE schedule) now or later this year… Changed “could be” to “will be”…
  2) Are there tools to display/analyze the raw sat imagery centered over the storm or any intermediate data (from various components of the HIE algorithm itself) Yes… we typically show the positions of the interpolated forecast position versus the HIE/ADT automated storm center determined position on our homepage, but positioning is not a requirement of the HIE… only intensity. I have added a slide to illustrate the possible positioning analysis that we currently do.

## Slide 9: ”Deep-Dive” Validation Tools
Graphical timeline example of HIE analysis versus observational data and/or TC forecast center Dvorak estimates
  Allows for quick analysis of the accuracy of the HIE performance versus subjective Dvorak estimates and/or “ground truth”
  Plots can be provided in real-time or in post-storm analysis mode
  SAB Dvorak estimates and NHC Best Track are displayed here
Timeline of HIE and SAB intensity estimates versus NHC Best Track
Notes:   For each product, describe and illustrate the “deep-dive” validation tools that you have or are developing. At a minimum address the following:
  - Capabilities (in their final state)
  - Intended use
  - Datasets used
  - Visualization software tools used (IDL, McIDAS, other…) to visualize the products, intermediate products, diagnostic data, product performance measures, reference/”ground-truth” data, etc…

## Slide 10: ”Deep-Dive” Validation Tools
Histograms of HIE and SAB intensity estimates differences versus NHC Best Track
Histogram of HIE and operational center intensity estimates differences from “ground truth”
  Provides easy display of errors between the two methodologies
  Can easily identify any biases in intensity differences in either set of estimates
  HIE versus SAB Dvorak intensity differences from NHC Best Track are shown in the graph to the right
Notes:   For each product, describe and illustrate the “deep-dive” validation tools that you have or are developing. At a minimum address the following:
  - Capabilities (in their final state)
  - Intended use
  - Datasets used
  - Visualization software tools used (IDL, McIDAS, other…) to visualize the products, intermediate products, diagnostic data, product performance measures, reference/”ground-truth” data, etc…

## Slide 11: ”Deep-Dive” Validation Tools
Display HIE automated storm center position versus “ground truth” and forecast interpolation positions
  Provides visual method to determine accuracy of automated storm center selection position
  Can be used to assess accuracy of current storm forecast from issuing TCFC
  Can be compared to aircraft reconnaissance, if available
Example of image displaying storm center location information.
HIE Determined
Reconnaissance
Forecast
Interpolation
Notes:   For each product, describe and illustrate the “deep-dive” validation tools that you have or are developing. At a minimum address the following:
  - Capabilities (in their final state)
  - Intended use
  - Datasets used
  - Visualization software tools used (IDL, McIDAS, other…) to visualize the products, intermediate products, diagnostic data, product performance measures, reference/”ground-truth” data, etc…

## Slide 12: “Deep-Dive” Validation Tools
Current intensity validation statistical output example
  Storm center positioning error analysis versus ‘ground truth” (either reconnaissance and/or NHC Best Track information)
  Accuracy and precision measurements are displayed for the storm in question or for entire ocean basin and season
  Comparisons with manual positions from TCFC can be output, if available
  Output layout mirrors output parameters as utilized in current operations by NOAA/SAB
POSITIONING ERRORS (distance in nmi)
OVERALL bias rmse aae stdv cnt
SAB:LAT 0.00 0.17 0.12 0.17 118
SAB:LON -0.07 0.24 0.17 0.23 118
SAB:DIST 13.86 118
ADT:LAT 0.04 0.22 0.17 0.22 118
ADT:LON -0.05 0.31 0.22 0.31 118
ADT:DIST 18.16 118
Estimated Position Error (nmi) by Fix Method
Method Num (%) ADT SAB
FORECAST 77 ( 65%) 20.1 14.9
SPIRAL 29 ( 24%) 16.8 13.9
COMBO 12 ( 10%) 8.9 7.2
EXTRAP 0 ( 0%) 0.0 0.0
OVERALL 118 18.2 13.9
Notes:   For each product, describe and illustrate the routine validation tools that you have or are developing. At a minimum address the following:
  - Capabilities (in their final state)
  - Datasets used
  - Visualization software tools used (IDL, McIDAS, other…) to visualize the products, intermediate products, diagnostic data, product performance measures, reference/”ground-truth” data, etc…
  -

## Slide 13: Ideas for the Further Enhancement and Utility of Validation Tools
Graphical and textual information could be sent to a webpage to allow for immediate, real-time viewing and investigation of HIE performance versus in situ measurements and/or additional subjective estimates of current tropical cyclone intensity and automated positioning accuracy
Statistical analysis of different tropical cyclone stages (formation, mature, dissipation) and HIE scene types (Curved Band, Central Dense Overcast, Eye, Shear, etc.) could be derived in real-time to allow HIE users to be aware of algorithm precision and accuracy during specific TC analysis situations.
  Analysis could also be derived for individual basins (North Atlantic, East/ Central Pacific) and storm seasons to indicate any additional precision and accuracy errors users should be aware of
Notes:   Please provide your thoughts and ideas for enhancing the capabilities and utililty of the validation tools beyond what you already planned to do. For example:
  1) Could your matchup databases support product reprocessing?
  2) What new visualization technologies could be used to further enhance the capability/utility of a routine or “deep-dive” validation tool?
  3) What web interfaces to your validation tool outcomes could/should be developed (if not already developed)?
  4) Other ideas?
  Comments (JD):
  1) What about tools to display any of the intermediate data from various components of the HIE (ie., like Spiral Centering; figure 2 in HIE ATBD)? Nope… nothing like that. We could derive something that displays the different locations (first guess, final center location, but that would require parsing of the output text in the bulletin (diagnostic output). Figure 2 is not an output… it is for illustrative purposes only.

## Slide 14: Summary
Validation of HIE intensity estimates are conducted versus either in situ aircraft reconnaissance measurements of TC maximum wind speed measurements or Best Track storm information provided from an official TC forecast center.
The HIE validation suite has already been utilized by an official, operational TC forecast center (NOAA/SAB) to verify the ADT/HIE against their Dvorak intensity estimates. The layout and information provided was specifically defined to meet their specifications for intensity estimate validation and is familiar to this and other TC forecast centers (and HIE project stakeholders).
HIE Validation results are easy to interpret and can be presented either textually or graphically (and can easily be implemented into any graphical display program).